BASSBOSS Digs Deep for More Bass in Compact Format with DJ21S Subwoofer

Portable, Affordable 21” BASSBOSS Sub Delivers Frequency Response Down to 24Hz with Plenty of Built-in Power

Austin, TX, May 22, 2017 — Premium loudspeaker manufacturer BASSBOSS has announced a brand new subwoofer designed for portability and impressive low-end response: the DJ21S, a single 21” powered subwoofer. The DJ21S is the perfect choice for delivering the deepest frequencies that any modern music requires, thanks to frequency response that goes all the way down to 24 Hz. The DJ21S is powerful and deep enough to perform without compromise and yet cost-effective enough for DJs who are providing their own sound reinforcement to bring intense bass in a passenger vehicle.

Deep bass, high output, small size and great value are the four things that make for the perfect portable subwoofer. The DJ21S takes bass reproduction to depths unattainable from even much larger subwoofers. DJ21S provides unprecedented cost to output, delivering the deep-bass SPL level of four or more competing subwoofers. The DJ21S provides every mobile DJ with an opportunity to bring bigger sound using less equipment, a smaller vehicle and less time and effort.

“The DJ21S is designed to deliver superb low frequency response at an accessible price point for DJs and installation applications that demand big performance but prefer a small cabinet,” says BASSBOSS president David Lee. “It’s a truly compact sub that can deliver the extreme depth demanded by today’s cutting-edge music, while maintaining critical listening clarity.”

Deeper by Design

The DJ21S provides maximum performance and value by bringing together a combination of superior quality components, each carefully selected for their specific advantages, and designing an enclosure around them that ensures maximum performance with minimal waste. The cabinet was carefully designed to minimize material costs and weight while delivering peak sound performance. The DJ21S’s new 21” woofer is designed to operate in smaller enclosures.

BASSBOSS chose a split-wound coil because it can produce more linear force through the range of movement of the cone, resulting in lower distortion and improved linearity at high output. The premium-quality driver features a split-wound, 4.5 inch, 4-layer, copper-clad aluminum voice coil, capable of peak-to-peak excursion of up to 60 mm. To take advantage of the massive displacement of the new 21” woofer, the vented enclosure is tuned to optimize extremely low frequency output using a large port. The port walls double as cabinet bracing and the port air flow serves to cool the amplifier. The total package weighs only 138 pounds, making it remarkably small and light for a subwoofer capable of 24Hz. At only 35 in. x 24 in. x 24 in., it can be transported by one person in a hatchback or small SUV.

Less is More

The DJ21S combines light and low with loud, offering 132 dB SPL of sustained output.  Its built-in amplifier supplies 2400 Watts of continuous RMS Class D power for plenty of headroom. The frequency response of the DJ21S is +-3dB from 24Hz to 90Hz, with the greatest output level, +2.5 dB, occurring at 30 Hz, where most portable subwoofers struggle to achieve specifications of -10 dB.

DSP Power for Peak Performance

The DJ21S features built-in, comprehensive DSP processing, including high-pass and low-pass filters, as well as proprietary BASSBOSS limiters and other protections to eliminate the risk of driver overload of any kind. The protection systems effectively prevent overheating of the voice coils and minimize long-term thermal compression while having virtually no effect on the transient response and peak output of the loudspeaker. No outboard equipment or processing is needed, only power and a signal source.

Built to Last and Last

With cabinets are constructed from 18mm Baltic Birch plywood and assembled using dado joints, screws, and advanced composite adhesives, the DJ21S is rugged enough to withstand load-in and load-out day after day. Stainless steel bolts are used to secure the drivers, amplifier and pole sockets for a lifetime of secure service. A durable black polyurethane coating serves as the cabinets long-lasting finish. A black powder-coated perforated steel grill protects the driver from damage. The woofer cones are waterproofed to guard against accidental exposure to rain, spilled drinks, or dust.

The new DJ21S is shipping now and priced at $2995.00 each.

About BASSBOSS
BASSBOSS creates premium, ultra high-fidelity sound systems for the professional consumer, live sound and systems integration markets. The company was founded on the design and engineering expertise of David Lee, a pioneer in subwoofer design whose work has transformed the audio systems for hundreds of venues across North America. BASSBOSS systems are easily integrated, compact and power-efficient. Each cabinet is highly optimized with dedicated, comprehensive amplification and processing. For more information on BASSBOSS, please visit www.bassboss.com

Press contact:

Jeff Touzeau

Public Relations

Hummingbird Media, Inc.

(914) 602-2913

jeff@hummingbirdmedia.com